## Slide 1
MIKROTIK
Unified Threat Management (UTM)
MIKROTIK
December 2025
Presented by Mark Jeryl H. Omandam BSIT-4

## Slide 2
Introduction.
MikroTik is an affordable and flexible networking platform powered by RouterOS, offering enterprise-level features such as routing, firewalling, NAT, VPN, bandwidth control, and hotspot services. It is widely used across homes, schools, businesses, and ISP networks, with configuration options suitable for both beginners and professionals. As a UTM solution, MikroTik integrates security and traffic management features into a single device, enabling it to function as both a router and a security gateway that protects, controls, and optimizes network performance in physical and virtual environments.
MikroTik UTM provides essential network security by integrating firewalling, traffic control, VPN, content filtering, and access management into a single RouterOS-based device.

## Slide 3
FEATURES
OF MIKROTIK

## Slide 4
  DHCP
  Automatically assigns IP addresses to devices
  Reduces manual network configuration
  Prevents IP address conflicts
  Makes network management easier

## Slide 5
  Go to IP → DHCP Server
  Click DHCP Setup
  Select the LAN interface (ether2)
  Set gateway, address pool, and DNS
  Finish the setup
Steps

## Slide 6
  Go to IP → DHCP Server
  Click DHCP Setup
  Select the LAN interface (ether2)
  Set gateway, address pool, and DNS
  Finish the setup
Steps

## Slide 7
  2. NTP (Network Time Protocol)
Synchronizes device clocks across the network
Ensures accurate logs and scheduled tasks
Functions as a local time server for LAN clients
Uses router's internal clock for reliability

## Slide 8
Steps
Go to System → NTP Server
Check "Enabled" and "Use Local Clock"
Set Local Clock Stratum to 5 and click Apply
On client PC, go to Internet Time Settings
Enter Server IP (10.10.10.1) and click Update now

## Slide 9
  3.Specific Device Ping Banned
  Blocks ICMP (ping) traffic
  Prevents network scanning
  Increases device-level security
  Allows selective device control

## Slide 10
  Go to IP → Firewall → Filter Rules
  Click +
  Set Chain: forward
  Enter source IP address of device
  Set Protocol: icmp
  Set Action: drop
  Save
Steps

## Slide 11
  Go to IP → Firewall → Filter Rules
  Click +
  Set Chain: forward
  Enter source IP address of device
  Set Protocol: icmp
  Set Action: drop
  Save
Steps

## Slide 12
  Go to IP → Firewall → Filter Rules
  Click +
  Set Chain: forward
  Enter source IP address of device
  Set Protocol: icmp
  Set Action: drop
  Save
Steps

## Slide 13
  4.IP Reservation
  Assigns permanent IP addresses to devices
  Uses MAC address binding
  Ensures consistent IP usage
  Useful for servers and important devices

## Slide 14
  Go to IP → DHCP Server → Leases
  Click +
  Enter IP Address
  Enter MAC Address
  Apply and OK
Steps

## Slide 15
  Go to IP → DHCP Server → Leases
  Click +
  Enter IP Address
  Enter MAC Address
  Apply and OK
Steps

## Slide 16
  5.Limit Bandwidth
  Controls internet speed per device
  Prevents bandwidth abuse
  Ensures fair network usage
  Improves overall performance

## Slide 17
  Go to Queues → Simple Queues
  Click +
  Set target IP address
  Set maximum upload and download speed
  Save
Steps

## Slide 18
  Go to Queues → Simple Queues
  Click +
  Set target IP address
  Set maximum upload and download speed
  Save
Steps

## Slide 19
  6.DNS Hostname Resolver
  Converts domain names to IP addresses
  Speeds up browsing
  Allows local hostname resolution
  Improves network reliability

## Slide 20
  Go to IP → DNS
  Add DNS servers (8.8.8.8, 1.1.1.1)
  Go to Static tab
  Click +
  Enter domain name and IP address
  Apply and OK
Steps

## Slide 21
  Go to IP → DNS
  Add DNS servers (8.8.8.8, 1.1.1.1)
  Go to Static tab
  Click +
  Enter domain name and IP address
  Apply and OK
Steps

## Slide 22
  7.Kid Control
  Kid Control is a feature that allows you to manage internet access for specific devices on your network, such as restricting access for children's devices during certain times. It allows you to create profiles that block internet connectivity based on a schedule (e.g., blocking access on specific days or hours).

## Slide 23
Steps
Go to IP → Kid Control.
Create a profile and set allowed time slots (e.g., 7 AM - 1 PM).
Go to Devices tab and click +.
Enter the child's device MAC Address.
Select the User Profile created earlier.
Click OK to activate.

## Slide 24
Steps
Go to IP → Kid Control.
Create a profile and set allowed time slots (e.g., 7 AM - 1 PM).
Go to Devices tab and click +.
Enter the child's device MAC Address.
Select the User Profile created earlier.
Click OK to activate.

## Slide 25
Conclusion
MikroTik is a powerful and cost-effective networking solution that combines routing, security, and traffic management features into a single platform. Through its RouterOS, it provides essential UTM functions such as DHCP, NAT, firewall filtering, bandwidth control, DNS management, and Kid Control. These features allow MikroTik to function not only as a router, but also as a security gateway that improves network stability, protects connected devices, and optimizes internet usage. Because of its flexibility and ease of configuration, MikroTik is well suited for laboratories, schools, small businesses, and real-world production networks.

## Slide 26
THANK YOU
MIKROTIK
December 2025